## Slide 1: Vehicle Stabilization
Joe Elliot
Joe Hansen
Craig Duck

## Slide 2: Stabilization
How does your agency handle vehicle stabilization?
Notes: 2

## Slide 3: Cribbing
Used to stabilize a vehicle
Lengths of wood used to prevent a vehicle from moving backward and forward.
Notes: 3

## Slide 4: Step Chocks
Placed under the side of the vehicle
  One toward front of vehicle
  One toward rear of vehicle
Notes: 4

## Slide 5: Box Crib
Standard cribbing can be used to form a box crib.
Place cribbing at right angles to the preceding layer of cribbing.
Notes: 5

## Slide 6: Wedges
Used to snug up loose cribbing or when using lift airbags
Should be the same width as the cribbing
Notes: 6

## Slide 7: Rescue Lift Air Bags
Used to lift a vehicle or object off a victim
Always use cribbing when using rescue lift air bags.
Notes: 7

## Slide 8: Low-Pressure Lift Air Bags
Often used in recovery operations
Sometimes used for vehicle rescue operations
Come in many shapes and sizes
Can be less stable until fully inflated
Notes: 8

## Slide 9: Medium-Pressure Lift Air Bags
Have either two or three cells inside their design
Best when used in aircraft or truck rescue
Notes: 9

## Slide 10: High-Pressure Lift Air Bags
Most common air bags used by the fire service for rescue work
Heavily constructed
Generally made of vulcanized rubber mats reinforced by steel
Notes: 10

## Slide 11
www.AfricaFireMission.org

## Slide 12: Materials utilized include:
Vehicle Stabilization
Copyright 2014 Jones & Bartlett Learning LLC and NFPA
Notes: 12